## Slide 1: TIQBio updates Feb-March
Simon

## Slide 2: Needs of AZ
Cancer Model
  Cell/spheroid viability
  Tumour size
  Morphology
  Cell death/apoptosis
  Proliferation
  Metabolism
  ECM deposition
Non-Cancer Model
  Fibrosis
  Regeneration
Interested in
  High throughput
  Lower requirement for sample prep (label-free!)

## Slide 3: Dual–illumination lightsheet
Designed Full system in CAD
Ordered: Optical components, Camera, Objectives, Stage.
To Do:
  Build system (parts still arriving)
  Electronics, Firmware and synchronisation
  Software

## Slide 4: Illumination
Sample chamber
10x 1NA objectives
3x beam expander / scan-tube lens
Gavlo scanner
50:50 beam splitter
Reflective collimator

## Slide 5: Detection
1NA 20x
Epiflourescence, or other illumination possible
Automated filter wheel
Hamamatsu camera (High QE)
100Hz imaging

## Slide 6: Stage + sample chamber
Multiple samples (up to 10?)
Heated
Piezo movement (20mm range)

## Slide 7
Camera A
Stage X
Galvo A
Galvo B
Laser AOTF
Environmental
Camera B
Stage Y
Stage Z
PC
PCIe
PCIe
USB
USB
USB
USB
Digital Out
Analog Out
Digital Out
Digital Out
Stage Controller
SPI Dual DAC
Analog Out
OpAmp
OpAmp
Digital Out
µC
Filter Wheel
Digital Out
Digital Out
µC
TBD
SPI Dual DAC
SPI Dual DAC
Analog Out
Analog Out
Analog Out
Analog Out
Supercontinuum
USB